## Slide 1
Presented By M6:
VINIT VIJAYKUMAR ADKE
YASH SANJAYKUMAR PARDESHI
JASWANTH GIRIDHARGOPALAN
DHIRRAJ SURESH KUMAR

## Slide 2
Maximize distance travelled using DOE
Identify key design parameters (factors)
Recommend a high-performance, cost- effective design

## Slide 3
Cars were released from the top of the ramp
Horizontal distance traveled from the end of the ramp to the car’s stopping point was measured
Procedure
Procedure
Randomized run order (generated by minitab)
2^4 full factorial * 3 replicates = 48 observations
Constraints
Used Lego pieces those were provided.
Car design included mandatory windshield, steering wheel.

## Slide 4
Big:
Back:
Large:
Big:
Length
Load Distribution
Width (Axle)
Tyre Size
Small:
Front:
Small:
Small:

## Slide 5
Randomization
Type Design
Replications
2^4 full factorial design
Run 3 replications to reduce noise
Randomized run order from Minitab
Response Variable
Horizontal distance travelled by the Lego car after leaving the ramp
UoM
cms
Set
Average of 3 repeated trails per design

## Slide 6
Significant Effects Identified:
Length (A): Strongly significant (p=0.000)
Width (C): Strongly significant (p=0.000) (Effect = 20.50, p = 0.000)
Length * Tyre Size(AD): Statistically significant (p=0.030)

## Slide 7
R-sq: 73.85% -> Strong proportion of the variability in the distance.
R-sq(adj): 61.59% -> Still shows decent model fit
R-sq(pred): 41.16% -> Moderate capability for predicting distance of new, untested design.
INTERPRETATION:
Good model fit, but potential for improvement in predictive performance

## Slide 8
Significant Factors:
Length (A), Width (C), and the interaction Length * Tyre Size (AD) -> Outside reference line -> Statistical Significance

## Slide 9
Normal Probability Plot: Points close to line -> residuals are normally distributed
Residuals vs Fits: Random scatter around zero -> constant variance
Histogram: Belly shaped -> Normality
Residuals vs Order: Points randomly scattered -> Errors are independent
CONCLUSION:
Suggests the model assumptions are adequately met.

## Slide 10
Length -> Strong +ve effect. Big Cars perform significantly better than small ones.
Load Distribution -> Front heavy designs slightly outperforms back-heavy ones -> Minimal Effect.
Width -> Large axle width greatly increases distance. Most influential factor..
Tyre Size -> Slightly –ve trend. No significant effect.

## Slide 11
Length * Load Distribution: Interaction exists, but not very strong
Length * Width: Strong Interaction
Length * Tyre Size: Slight Interaction
Load Distribution * Width: Significant Interaction
Load Distribution * Tyre Size: Minor Interaction.
Width * Tyre Size: Small Interaction

## Slide 12
Big Length + Back Load + Large Width + Small Tyres = 151.33 cms
Big Length + Large Width -> Main effects
Small Tyres -> Regression & Interaction
Back Load -> Enhances performance

## Slide 14
Length
Load Distribution
Width
Tyre Size
Distance
Big
Back
Large
Small
151.33 cms23800
Total Cost
$ 23800
151.33 cms

## Slide 15
DOE is powerful. It helps not just individual effects, but how variables interact.
The importance of randomization and replication to eliminate bias and noise
Minitab and visualization tools make interpretation and decision-making easier
Validate models using ANOVA, residual analysis & regression
Notes: Photo by Eric & Niklas on Unsplash